Da teoria à prática em Service Mesh com Istio e Openshift.

---
Cléber da Silveira
Arquiteto de Software Java.
Entusiasta DevOps.
Apreciador de Cloud Computing.

---
Service Mesh
Service Mesh
“Service Mesh é uma camada de infraestrutura dedicada para lidar com a comunicação de serviço a serviço.
Na prática, a malha de serviço é normalmente implementada como uma matriz de proxies de rede leves que são implementados junto com o código do aplicativo, sem que o aplicativo precise estar ciente.”
William Morgan, Buoyant’s CEO.

---
Service Discovery e Circuit Breakers - Abordagem Inicial
Service Discovery e Circuit Breakers - Abordagem Inicial

---
Service Discovery and Circuit Breakers - Abordagem Inicial
Service Discovery and Circuit Breakers - Abordagem Inicial
Bibliotecas sofisticadas tornaram-se muito populares como forma de evitar reescrever a mesma lógica em todos os serviços.

---
Problemas dessa abordagem
Problemas dessa abordagem
As organizações ainda precisam investir tempo de sua equipe de engenharia na construção da cola que liga as bibliotecas ao restante de seu ecossistema.
Limita as ferramentas, as runtimes e as linguagens que você pode usar para seus microsserviços. Bibliotecas para microsserviços são frequentemente escritas para uma plataforma específica.
Certificar-se de que milhares de instâncias de serviços estejam usando as mesmas ou, pelo menos, versões compatíveis de sua biblioteca, não é trivial, e cada atualização significa integrar, testar e reimplementar todos os serviços.

---
Sidecar – Abordagem Inicial
Sidecar – Abordagem Inicial
Processo auxiliar que executa ao lado seu aplicativo e fornece recursos extras.
Essas implementações de proxy de código aberto tendem a ser projetadas para funcionar com componentes de infraestrutura específicos

---
Service Mesh
Service Mesh

---
Caso de Uso.
Caso de Uso.

---
Istio Architecture
Istio Architecture
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Service Mesh
Service Mesh
O tráfego de serviço ainda flui de proxy para o proxy diretamente, mas o plano de controle conhece cada instância do proxy, também gerencia o controle de acesso e a coleta de métricas.

---
Mixer
Mixer
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Pilot
Pilot
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Benefícios de gerenciamento de tráfego
Benefícios de gerenciamento de tráfego
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Bookinfo - Istio
Bookinfo - Istio
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Exemplo de Fallback sem Istio
Exemplo de Fallback sem Istio
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Exemplo de Fallback sem Istio
Exemplo de Fallback sem Istio
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Canary no Istio
Canary no Istio
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Bookinfo - Istio
Bookinfo - Istio
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Bookinfo - Istio
Bookinfo - Istio
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Bookinfo - Istio
Bookinfo - Istio
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Bookinfo - Istio
Bookinfo - Istio
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Como isso acontece no Openshift ?
Como isso acontece no Openshift ?
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Como isso acontece no Openshift ?
Como isso acontece no Openshift ?
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Como isso acontece no Openshift ?
Como isso acontece no Openshift ?
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Como isso acontece no Openshift ?
Como isso acontece no Openshift ?
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Como isso acontece no Openshift ?
Como isso acontece no Openshift ?
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Como isso acontece no Openshift ?
Como isso acontece no Openshift ?
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Como isso acontece no Openshift ?
Como isso acontece no Openshift ?
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Como isso acontece no Openshift ?
Como isso acontece no Openshift ?
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Como isso acontece no Openshift ?
Como isso acontece no Openshift ?
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Grafana lendo do Prometheus
Grafana lendo do Prometheus
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Grafana lendo do Prometheus
Grafana lendo do Prometheus
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Grafana lendo do Prometheus
Grafana lendo do Prometheus
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Prometheus
Prometheus
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
jaeger tracing
jaeger tracing
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
jaeger tracing
jaeger tracing
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
jaeger dependencies
jaeger dependencies
[Speaker Notes: Envoy Istio uses an extended version of the Envoy proxy, a high-performance proxy developed in C++, to mediate all inbound and outbound traffic for all services in the service mesh. Istio leverages Envoy’s many built-in features such as dynamic service discovery, load balancing, TLS termination, HTTP/2 & gRPC proxying, circuit breakers, health checks, staged rollouts with %-based traffic split, fault injection, and rich metrics. Envoy is deployed as a sidecar to the relevant service in the same Kubernetes pod. This allows Istio to extract a wealth of signals about traffic behavior as attributes, which in turn it can use in Mixer to enforce policy decisions, and be sent to monitoring systems to provide information about the behavior of the entire mesh. The sidecar proxy model also allows you to add Istio capabilities to an existing deployment with no need to rearchitect or rewrite code. You can read more about why we chose this approach in our Design Goals. Mixer Mixer is a platform-independent component responsible for enforcing access control and usage policies across the service mesh and collecting telemetry data from the Envoy proxy and other services. The proxy extracts request level attributes, which are sent to Mixer for evaluation. More information on this attribute extraction and policy evaluation can be found in Mixer Configuration. Mixer includes a flexible plugin model enabling it to interface with a variety of host environments and infrastructure backends, abstracting the Envoy proxy and Istio-managed services from these details. Pilot Pilot provides service discovery for the Envoy sidecars, traffic management capabilities for intelligent routing (e.g., A/B tests, canary deployments, etc.), and resiliency (timeouts, retries, circuit breakers, etc.). It converts a high level routing rules that control traffic behavior into Envoy-specific configurations, and propagates them to the sidecars at runtime. Pilot abstracts platform-specifc service discovery mechanisms and synthesizes them into a standard format consumable by any sidecar that conforms to the Envoy data plane APIs. This loose coupling allows Istio to run on multiple environments (e.g., Kubernetes, Consul/Nomad) while maintaining the same operator interface for traffic management. Istio-Auth Istio-Auth provides strong service-to-service and end-user authentication using mutual TLS, with built-in identity and credential management. It can be used to upgrade unencrypted traffic in the service mesh, and provides operators the ability to enforce policy based on service identity rather than network controls. Future releases of Istio will add fine-grained access control and auditing to control and monitor who accesses your service, API, or resource, using a variety of access control mechanisms, including attribute and role-based access control as well as authorization hooks.]

---
Obrigado.
@csilveir
csilveir
clebers@dbserver.com.br